## Slide 1: Los Angeles County MS4 Permit Reissuance: New Directions & Strategy
Presented by
LA Regional Water Quality Control Board
Southern California Water Dialogue Meeting
June 22, 2011

## Slide 2: Outline
Permit Structure
Permit Requirements
  Standard Provisions
  TMDL Provisions
  Monitoring Program Considerations
  Reporting Program Considerations
Tentative Schedule
  Opportunities for input
Q & A / Discussion

## Slide 3: Background
Last issued in 2001
Reopened in 2006, 2007 and 2009 to incorporate TMDL provisions
Amended in April 2011 to void and set aside 2006 provisions in response to writ of mandate
Reissuance scheduled for 2012
Notes: Last issued on cusp of TMDL development in 2001
TMDL – total maximum daily loads – plan to achieve water quality standards where water quality impairment has been identified –
Characterizes problem, identifies numeric targets necessary to achieve water quality standards, identifies sources of pollutants, links sources to water quality impairment, allocates allowable loads to point and nonpoint sources of the pollutant.

## Slide 4: Permit Structure: Background
Single permit for 84 cities, LA County & LACFCD
  Los Angeles County Flood Control District role
  (LA County Flood Control Act)
  Highly interconnected system across jurisdictional boundaries
  Commingled discharges to receiving waters
  Opportunities for cooperation
  Consistency & efficiency in public outreach, monitoring & reporting
Notes: 1915 Flood Control Act, established LACFCD
3000 mi2
500 mi open channel
2800 mi underground storm drain
120000 catch basins

## Slide 5: Permit Structure: New Directions
Establish core program requirements for all Permittees
Complement local initiatives / ordinances
Provide flexibility to tailor efforts to relevant water quality problems in watershed / community
Allow coordination among Permittees on watershed basis

## Slide 6: New Directions: Watershed-based Permitting
New permit requirements based on watershed TMDLs
  Aggregate wasteload allocations assigned to MS4 Permittees within a watershed
  Joint implementation plans developed by multiple Permittees
LA County Flood Control District Funding Initiative (AB 2554)
Notes: Currently soliciting input from permittees on permit structure –
Initial feedback at Kickoff meeting on May 25, 2011
Systematic feedback through on-line survey to Permittees, responses due next week.
Thus far all respondents have been in favor of a watershed based permitting – some suggesting a single permit with watershed chapters, others suggesting multiple watershed-based permits – in each case,
Permit structure would continue to recognize the highly interconnected system and commingled discharges – and would provide opportunities for coordination among permittees
Permit structure would also support watershed-based TMDL implementation efforts

## Slide 7: Permit Provisions: Key Requirements
Non-stormwater Discharge Prohibition
  Into MS4 and watercourses
  Some exceptions if (1) not a source of pollutants and (2) consistent with antidegradation policies and (3) TMDLs
Receiving Water Limitations
  Standard “Do Not Cause or Contribute” Language from State Board Precedential Orders
Core Program Elements
TMDL Provisions
Monitoring & Reporting
Notes: Discharges from the MS4 that cause or contribute to a violation of WQS are prohibited.

## Slide 8: Permit Provisions: Core Elements
IC/IDE Program
Construction Activities
Industrial / Commercial Facilities
Public Agency Activities
Public Information & Participation
New/Redevelopment Planning
Notes: 6 core program elements

## Slide 9: New/Redevelopment Planning
THEN
Post-development peak flow control in natural drainage systems
Post-construction treatment control BMPs
  85th percentile 24-hour runoff event
  80% annual runoff volume
  Runoff volume from ¾” storm event
NOW
Reduce ‘Effective Impervious Area’ (EIA) to <= 5% project area
On-site retention of water quality design volume
  Hierarchy of BMPs
    Infiltration/ET/Reuse
    Biofiltration (1.5x to achieve equivalent load reduction)
    Treatment
  Off-site mitigation
Hydromodification control
  LID may satisfy for some projects

## Slide 10: New/Redevelopment: Key Areas for Discussion
LID implementation metrics
  Effective Impervious Area (EIA) limitation
  Volume based on-site retention standard
BMP hierarchy (Retention, Biofiltration, Treatment)
Infeasibility criteria
Offsite mitigation requirements
  Location, mitigation ratios, project types
Alternative post-construction regional plan
  Substitutes for part or all of on-site post-construction BMPs
Existing local LID ordinances

## Slide 11: New Development/ Redevelopment Alternatives
Ventura MS4 Requirements
Modified current RB approach
  Incorporation of elements of local LID ordinances
Incorporation of other requirements
  Other Regional Boards’ LID approaches
  Other states’ approaches

## Slide 12: TMDL Provisions: Background
23 TMDLs with MS4 WLAs in effect for LA County
  2007 & 2009 amendments
    MDR Bacteria TMDL – Summer WLAs
    LA River Watershed Trash TMDL WLAs
6 other TMDLs in approval process

## Slide 13: TMDL Provisions: Considerations
Federal regulations require provisions consistent with assumptions & requirements of WLAs
  Focus on WLA deadlines within permit term
Numeric water quality based effluent limitations (WQBELs) vs. BMP based requirements

## Slide 14: TMDL Provisions: LA River Trash WLAs Example
Numeric water quality based effluent limitations
  Equivalent to WLAs
  Compliance measure if partial capture and/or institutional strategies are used
  Necessary absent “up-front” demonstration that controls will achieve TMDL design/performance standard
BMP based requirements
  TMDL design/ performance standard to achieve WLAs = full capture systems
  Compliance measure = % drainage area addressed by full capture systems
Notes: Full capture systems must meet certain design criteria – 1 year, 1 hour storm, 5 mm mesh screen
Annual volume of trash discharged from Permittee’s jurisdiction, based on estimation of trash generation

## Slide 15: TMDL Provisions: Considerations
Not one-approach-fits-all
  Stormwater vs. non-stormwater discharges
  TMDL implementation plans
  Other robust demonstrations that BMP performance will achieve WLAs

## Slide 16: Monitoring Program Considerations
Objectives
  Assess program effectiveness
  Determine Permittee compliance
Receiving water & ms4 outfall monitoring
Watershed/subwatershed-based design
Coordination with TMDL compliance monitoring requirements

## Slide 17: Reporting Program Considerations
Objectives
  Assess Program Effectiveness
  Guide Program Improvements
  Determine Permittee Compliance
Receiving Water Limitations compliance reporting criteria
  Targeted, specific program revisions
  Detailed implementation schedule
BMP performance demonstrations
  Collectively for outfall drainage
  Individually
Implementation Actions
  TMDL Implementation Plans
  Water Quality Improvement Plans
Notes: Effectiveness Assessment Guidance
  CASQA
  USEPA
  State Board

## Slide 18: Tentative Schedule
May 2011: Kick-off meeting
Aug.-Oct.: 1-2 issue-based workshops
Nov.-Jan.: 1-2 issue/general workshops
Jan. 2012: Draft permit
April 2012: Board hearing

## Slide 19: Opportunities for Input
Today’s meeting
Issue-based workshops
  New / Redevelopment Provisions
  TMDL Provisions
  Monitoring & Reporting Program
  Others?
Watershed-based meetings upon request
Individual meetings upon request

## Slide 20: Questions?
  Ivar Ridgeway, Chief
  Stormwater Permitting Unit
  (213) 620-2150
  iridgeway@waterboards.ca.gov
  Renee Purdy, Chief
  Regional Programs Section
  (213) 576-6622
  rpurdy@waterboards.ca.gov