## Slide 1: History of Salinity Management in Southern California
By
Richard Atwater
March 23, 2011

## Slide 2: Arid Climates – Salinity
Mediterranean Region
Mid-East
Southern Africa
Australia
Southwest US

## Slide 3: What is Salt?
Mineral salts (total dissolved solids)
Impacts
  Hardness (primarily calcium and magnesium)
    Plumbing Fixtures/Industrial uses/irrigation
    Soap Impacts
An Ions | Cat Ions
NA Sodium | Chloride
Calcium | Magnesium
Potassium | Sulfates

## Slide 4: Water Softening
Reduces hardness, but adds salt to water (exchange sodium in with calcium and magnesium) alternative is potassium
“Bad for irrigation”
MWD in the 1950’s “softened” Colorado River water” at the Weymouth Water Treatment Plant

## Slide 5: Southern California Map
TDS
SWP | 200-450 mg/L
Colorado River | 500-700 mg/L
Groundwater | 200-800 mg/L
Wastewater | 500-1000 mg/L

## Slide 6: Quick History of Efforts to Control Salinity
LACSD built brine line to Kaiser Steel mill and SCE Entiwanda power plant and Weymouth TP to bypass upstream water recycling plants
President Nixon treaty with Mexico for Colorado River “Minute 242”
1972 Colorado River Salinity Control Act
Mid-1970’s State Water Project began
Regional Boards “Basin Plans” required use of SWP (e.g., Santa Ana River)
Santa Ana River Brine line (1970s built to export salt )

## Slide 7: Regional Salinity Management Efforts
1990s 1997 1999 | Groundwater desalters 500 mg/L blending strategy MWD adopts Salinity Management Action Plan
2000 | Southern California Salinity Council formed
2001 | Multi-State Salinity Council
2002-11 | Funding and Control of Sources of Salinity ---brine concentrate research, water softener ordinances and rebates, watershed management strategies (e.g., Calleguas Creek )

## Slide 8: Salinity Management Study
MWD and US Bureau of Reclamation funded
Regional collaborative study (1997-1999)
Comprehensive analysis of salinity problems
Evaluation of alternatives and strategies
Recommended Policy (source control on CR and SWP, watershed solutions, brine and desalter projects)
Action Plan—Salinity Coalition advocacy, research, legislation, funding.

## Slide 9: Irrigation Salt Management Assistance
Salinity Guide for Irrigation (NWRI and WateReuse)
Recycled Water Training and Technical Assistance
Ongoing Research on Irrigation Practices at Cal Poly Pomona, UCR, and UC Davis
Plant science and irrigation management (Rancho Santa Ana Botanical Gardens)

## Slide 10: Other Salinity Coalition Activities
Regional Boards Salt and Nutrient Management Plans from the SWRCB Recycled Water Policy (2009)
Brine Concentrate research
Pre-treatment and wastewater treatment strategies (SCAP)
Membrane technologies and other low energy salt removal technologies

## Slide 11: Future
Update 1999 MWD Salinity Plan
AB1366 allows regulation of water softeners
Drought and water shortages
More water recycling and groundwater desalting, brine management strategies and zero liquid discharge
Comprehensive salinity management strategies need to be updated every decade

## Slide 12: Salinity Fundamentals:
Removing Salt from Water Uses A Lot of Energy
It is therefore, relatively expensive
Prevention is much more cost effective

## Slide 13: Salinity ---arid climates always a problem!
Salinity has been a water quality problem for over 100 years in so. California
Salinity will continue to be a critical water quality problem for the next 100 years.
Regional watershed management strategies and collaboration needed to manage salinity within the coastal plain of So. California.