## Slide 1: 2015 IRP Technical Process Draft Results
Southern California Water Dialogue
September 23, 2015

## Slide 2: Phase 1: IRP Technical Update Process and Schedule
Mar
Aug
Sep
Oct
Nov
Dec
Apr
May
Jun
Jul
Feb
2015
Technical
Technical Review and Update
Analysis
Draft Report
Member Agency
Member Agency Technical Process
Board
Oral Report
Consider Adoption
Updates to IRP Committee
Establish IRP Committee
Public Outreach Workshop
Notes: Internal Process –
Ongoing
MA Technical Process –
MA workgroup meetings twice a month April through August, as needed through October
WUE meetings monthly standing meeting April through July
Board –
Reporting in Feb and March (IRP Committee)
Monthly Updates from MA tech process
Wrapping up around the end of the year, head into Board Policy Process
Following slides breakdown activities at Board and MA levels

## Slide 3: Phase 2: IRP Policy Implementation Update Process and Schedule
Public
Public Outreach and Input
Member Agency
Member Agency Process
Board
Board Deliberation on Policy and Implementation
Mar
…
Apr
May
Jun
Feb
Jan
2016
Published Report
Notes: Internal Process –
Ongoing
MA Technical Process –
MA workgroup meetings twice a month April through August, as needed through October
WUE meetings monthly standing meeting April through July
Board –
Reporting in Feb and March (IRP Committee)
Monthly Updates from MA tech process
Wrapping up around the end of the year, head into Board Policy Process
Following slides breakdown activities at Board and MA levels

## Slide 4: Four Key Framing Questions
What is our current outlook on supplies and demands?
What happens if we do nothing?
What happens if we continue developing the current 2010 IRP targets?
What potential changes to the current 2010 IRP targets are needed?

## Slide 5: What is Our Current Outlook on Supplies and Demands?

## Slide 6: Conservation Savings

## Slide 7: Conservation Savings* Projected on 1990 Base Year
*Does not include conservation from Price Effect
Chart: Calendar Year
| 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040
System Loss | 42959.6481 | 43505.412 | 44051.1758 | 44596.9397 | 45142.7036 | 45686.93 | 46231.1565 | 46775.3829 | 47319.6093 | 47863.8358 | 48381.1877 | 48898.5396 | 49415.8914 | 49933.2433 | 50450.5952 | 50869.4435 | 51288.2917 | 51707.1399 | 52125.9882 | 52544.8364 | 53153.8789 | 53762.9213 | 54371.9637 | 54981.0062 | 55590.0486
Code-Based | 378454.6917 | 400381.159 | 416147.784 | 433876.7791 | 449854.9823 | 463334.5835 | 478782.2689 | 493633.9685 | 507573.4445 | 519020.6657 | 529710.9997 | 540421.8794 | 549660.0808 | 560262.0589 | 569281.2167 | 576610.4551 | 583632.4353 | 590588.4719 | 597435.915 | 604649.6307 | 622530.8325 | 629420.4013 | 636343.5043 | 643232.9931 | 649749.7455
Active | 192153.8785 | 176282.4241 | 166882.4188 | 153429.2621 | 140791.6496 | 132491.3367 | 123471.4992 | 114560.685 | 106883.6156 | 100046.2338 | 95321.276 | 90726.1158 | 87437.8753 | 81961.0388 | 76528.1774 | 74927.2865 | 73506.5535 | 71205.9791 | 67202.5308 | 58951.4563 | 40964.8473 | 40964.765 | 40964.7074 | 40964.6671 | 40927.0582
Conservation Savings* (Thousand Acre-Feet) |  |  |  | 
2020 | 2025 | 2030 | 2035 | 2040
636 | 667 | 696 | 716 | 746
Active
Code Based
System Loss

## Slide 8: Retail Demands

## Slide 9: Total Retail Demands Key Assumptions
Updated demographic forecasts
  SCAG RTP 12
  SANDAG Series 13
Retail M&I Demand
  New econometric model
Agency provided demand forecasts
  Agricultural
  Seawater Barrier
  Replenishment

## Slide 10: IRP Draft Forecast Total Retail Demand Historical and Projected
Chart: Calendar Year
Historical Production | 4486727.837 | 4282443.0855 | 4609484.5542 | 4425657.4154 | 4603835.0605 | 4350782.8514 | 4657451.4806 | 4773084.7751 | 4459358.8254 | 4259700.8159 | 4047454.9265 | 4102631.6585 | 4271346.0997 | 4359659.0149
2015 IRP Draft Forecast | 4278379.9205 | 4464581.3831 | 4590239.3577 | 4677764.8732 | 4760846.7831 | 4812568.4014 | 4840529.5316 | 4869737.54 | 4898461.6957 | 4927504.5816 | 4929895.8013 | 4951643.0568 | 4973539.7435 | 4995270.5508 | 5015769.5608 | 5034534.7146 | 5054729.295 | 5074796.6212 | 5093919.2613 | 5111230.467 | 5124660.33 | 5135936.8114 | 5154207.3623 | 5172511.3182 | 5190781.7102 | 5208642.9182
Historical Production | 4232926.2786 | 4009336.408 | 4314915.6243 | 4106986.489 | 4260925.2113 | 3986589.9189 | 4275581.6852 | 4374066.3868 | 4045507.9387 | 3823831.9431 | 3589078.4433 | 3626178.082 | 3781121.9319 | 3850977.9411
2015 IRP Draft Forecast | 3726467.3516 | 3851013.1648 | 3970070.3626 | 4050683.4945 | 4128943.8022 | 4176779.0659 | 4199016.6813 | 4221252.6154 | 4243491.6593 | 4265727.9121 | 4262965.0659 | 4278229.5934 | 4293493.2088 | 4308756.7033 | 4323613.2198 | 4338274.7253 | 4352322.1099 | 4366369.3407 | 4380417.6703 | 4394466.033 | 4408514.4066 | 4419287.2527 | 4430059.2747 | 4440831.1429 | 4451603.044 | 4462376.0659
Pre-Conservation
Post-Conservation

## Slide 11: Near-Term Demand Adjustment Key Assumptions
Capture observed reduction in demand
Estimate behavioral and structural elements
Adjust climate effects and other conservation savings elements to avoid double-counting of reductions in the forecast

## Slide 12: Retail Demands Post-Conservation Historical and Projected
Chart: Calendar Year
Blank | 3678091 | 3781515 | 3866540 | 3892160 | 3881601 | 3790448 | 3809724 | 3828998 | 3848272 | 3867541 | 3861808 | 3875116 | 3888423 | 3901729 | 3914629 | 3927333 | 3939504 | 3951675 | 3963846 | 3976018 | 3988189 | 3997690 | 4007189 | 4016689 | 4026189 | 4035690
Draft Adjusted Forecast Range | 84495 | 121347 | 180729 | 276677 | 431646 | 674144 | 679348 | 684554 | 689764 | 694979 | 700198 | 703622 | 707047 | 710472 | 713897 | 717323 | 720594 | 723864 | 727136 | 730407 | 733678 | 735894 | 738109 | 740325 | 742540 | 744756
Historical Production | 4232926.2786 | 4009336.408 | 4314915.6243 | 4106986.489 | 4260925.2113 | 3986589.9189 | 4275581.6852 | 4374066.3868 | 4045507.9387 | 3823831.9431 | 3589078.4433 | 3626178.082 | 3781121.9319 | 3850977.9411
2015 IRP Draft Adjusted Forecast | 3726467.4615 | 3851012.6484 | 3970070.9011 | 4050683 | 4128943.6044 | 4176779.5275 | 4199016.6813 | 4221252.8571 | 4243491.4615 | 4265728.1648 | 4262964.7253 | 4278229.7253 | 4293493.6703 | 4308756.6264 | 4323613.2967 | 4338274.9341 | 4352322.3187 | 4366369.6703 | 4380418.0879 | 4394466.4725 | 4408513.9451 | 4419286.9121 | 4430058.8901 | 4440830.9121 | 4451602.9451 | 4462375.9451
Range of Total Retail Demands (Million Acre-Feet) |  |  |  |  | 
 | 2020 | 2025 | 2030 | 2035 | 2040
Min | 3.79 | 3.86 | 3.93 | 3.99 | 4.03
Avg | 4.18 | 4.26 | 4.34 | 4.41 | 4.46
Max | 4.46 | 4.56 | 4.64 | 4.72 | 4.78

## Slide 13: Local Supplies

## Slide 14: Total Average-Year Local Supplies 2015 IRP Draft Forecast
Chart: Calendar Year
| 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040
Groundwater | 1280156.022 | 1282290.978 | 1290613.0549 | 1309688.7253 | 1308101.3516 | 1310108.4615 | 1311358.978 | 1312095.967 | 1312927.3077 | 1314288.4286 | 1315931.5604 | 1317158.4396 | 1318152.4725 | 1319642.0989 | 1321220.2967 | 1320892.044 | 1320060.6154 | 1319578.5275 | 1320059.989 | 1319903.8571 | 1320628.1209 | 1321415.011 | 1322143.956 | 1322346.2747 | 1322196.9341
Recycling | 386606 | 400582 | 410595 | 419015 | 425131 | 430503 | 435501 | 440176 | 444711 | 449015 | 453250 | 457434 | 461607 | 465358 | 468862 | 472331 | 475320 | 478204 | 481022 | 483669 | 486162 | 488597 | 491015 | 493433 | 495698
Los Angeles Aqueduct | 242631.7802 | 253579.6044 | 255992.0989 | 259074.8242 | 261100.4945 | 262205.4066 | 263071.1319 | 263435.8462 | 263760.4615 | 264035.022 | 264276.4066 | 264348.8791 | 264275.033 | 264382.6593 | 264296.3297 | 264651.3846 | 265083.989 | 265434.011 | 265899.5824 | 265924.3187 | 266121.5275 | 266296.8132 | 266945.7582 | 266638.6813 | 267637.4615
Groundwater Recovery | 126312 | 130339 | 134983 | 138800 | 142286 | 145404 | 148241 | 150920 | 153008 | 154189 | 155185 | 156177 | 157166 | 158017 | 158816 | 159565 | 160188 | 160758 | 161266 | 161694 | 162065 | 162319 | 162443 | 162567 | 162688
Surface Production | 108425.7363 | 113705.3626 | 113705.3626 | 113705.3626 | 113705.3626 | 113705.3626 | 113705.3626 | 113705.3626 | 113705.3626 | 113705.3626 | 113705.3626 | 113705.3626 | 113705.3626 | 113705.3626 | 113705.3626 | 113705.3626 | 113705.3626 | 113705.3626 | 113705.3626 | 113705.3626 | 113705.3626 | 113705.3626 | 113705.3626 | 113705.3626 | 113705.3626
Seawater Desalination | 50637.3626 | 50637.3626 | 50637.3626 | 50637.3626 | 50637.3626 | 50637.3626 | 50637.3626 | 50637.3626 | 50637.3626 | 50637.3626 | 50637.3626 | 50637.3626 | 50637.3626 | 50637.3626 | 50637.3626 | 50637.3626 | 50637.3626 | 50637.3626 | 50637.3626 | 50637.3626 | 50637.3626 | 50637.3626 | 50637.3626 | 50637.3626 | 50637.3626
Groundwater
Groundwater Recovery
Recycling
Surface Production
Seawater Desalination
LAA

## Slide 15: Total Average-Year Local Supplies 2015 IRP Draft Forecast
Chart: Calendar Year
| 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040
Blank | 1945042 | 1989597 | 1997482 | 2026887 | 2014675 | 2022733 | 2069010 | 2073748 | 2079837 | 2085670 | 2091007 | 2118439 | 2124325 | 2106316 | 2111965 | 2126956 | 2129472 | 2135303 | 2132152 | 2166652 | 2163889 | 2157676 | 2178060 | 2180579 | 2182670
Range | 547247 | 540008 | 555785 | 560137 | 582043 | 584130 | 546528 | 549988 | 551328 | 552408 | 553512 | 532589 | 532763 | 557176 | 557104 | 545849 | 553219 | 550690 | 557383 | 525323 | 531834 | 545139 | 527774 | 528012 | 528247
Total Local Supplies | 2194768.9011 | 2231134.3077 | 2256525.8791 | 2290921.2747 | 2300961.5714 | 2312563.5934 | 2322514.8352 | 2330970.5385 | 2338749.4945 | 2345870.1758 | 2352985.6923 | 2359461.044 | 2365543.2308 | 2371742.4835 | 2377537.3516 | 2381782.1538 | 2384995.3297 | 2388317.2637 | 2392590.2967 | 2395533.9011 | 2399319.3736 | 2402970.5495 | 2406890.4396 | 2409327.6813 | 2412563.1209

## Slide 16: Total Range of Local Supplies 2015 IRP Draft Forecast
Chart: Calendar Year
| 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040
Blank | 1945042 | 1989597 | 1997482 | 2026887 | 2014675 | 2022733 | 2069010 | 2073748 | 2079837 | 2085670 | 2091007 | 2118439 | 2124325 | 2106316 | 2111965 | 2126956 | 2129472 | 2135303 | 2132152 | 2166652 | 2163889 | 2157676 | 2178060 | 2180579 | 2182670
Range | 547247 | 540008 | 555785 | 560137 | 582043 | 584130 | 546528 | 549988 | 551328 | 552408 | 553512 | 532589 | 532763 | 557176 | 557104 | 545849 | 553219 | 550690 | 557383 | 525323 | 531834 | 545139 | 527774 | 528012 | 528247
Total Local Supplies | 2194768.9011 | 2231134.3077 | 2256525.8791 | 2290921.2747 | 2300961.5714 | 2312563.5934 | 2322514.8352 | 2330970.5385 | 2338749.4945 | 2345870.1758 | 2352985.6923 | 2359461.044 | 2365543.2308 | 2371742.4835 | 2377537.3516 | 2381782.1538 | 2384995.3297 | 2388317.2637 | 2392590.2967 | 2395533.9011 | 2399319.3736 | 2402970.5495 | 2406890.4396 | 2409327.6813 | 2412563.1209
Total Range of Local Supplies (Million Acre-Feet) |  |  |  |  | 
 | 2020 | 2025 | 2030 | 2035 | 2040
Min | 2.02 | 2.09 | 2.11 | 2.17 | 2.18
Avg | 2.30 | 2.35 | 2.38 | 2.40 | 2.41
Max | 2.62 | 2.64 | 2.67 | 2.69 | 2.71

## Slide 17: Imported Supplies

## Slide 18: CRA Base Supply Programs 2015 IRP Draft Forecast
Chart: Calendar Year
| 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040
Basic Apportionment - Adjustments | 474627 | 464714 | 461384.6154 | 461769.2308 | 461769.2308 | 461769.2308 | 462153.8462 | 462153.8462 | 462153.8462 | 461384.6154 | 461769.2308 | 461384.6154 | 461769.2308 | 461384.6154 | 461769.2308 | 437246.8462 | 436860.2308 | 436473.6154 | 436856.2308 | 431469.6154 | 431083 | 431465.6154 | 431464.6154 | 431078 | 426076
IID-SDCWA | 100000 | 100000 | 130000 | 160000 | 192500 | 205000 | 202500 | 200000 | 200000 | 200000 | 200000 | 200000 | 200000 | 200000 | 200000 | 200000 | 200000 | 200000 | 200000 | 200000 | 200000 | 200000 | 200000 | 200000 | 200000
IID-MWD | 85000 | 85000 | 85000 | 85000 | 85000 | 85000 | 85000 | 85000 | 85000 | 85000 | 85000 | 85000 | 85000 | 85000 | 85000 | 85000 | 85000 | 85000 | 85000 | 85000 | 85000 | 85000 | 85000 | 85000 | 85000
Canal Lining SDCWA | 81700 | 81700 | 81700 | 81700 | 81700 | 81700 | 81700 | 81700 | 81700 | 81700 | 81700 | 81700 | 81700 | 81700 | 81700 | 81700 | 81700 | 81700 | 81700 | 81700 | 81700 | 81700 | 81700 | 81700 | 81700
Canal Lining MWD | 16000 | 16000 | 16000 | 16000 | 16000 | 16000 | 16000 | 16000 | 16000 | 16000 | 16000 | 16000 | 16000 | 16000 | 16000 | 16000 | 16000 | 16000 | 16000 | 16000 | 16000 | 16000 | 16000 | 16000 | 16000
PVID | 30000 | 30000 | 30000 | 30000 | 30000 | 30000 | 30000 | 30000 | 30000 | 30000 | 30000 | 30000 | 30000 | 30000 | 30000 | 30000 | 30000 | 30000 | 30000 | 30000 | 30000 | 30000 | 30000 | 30000 | 30000
SNWA | 60000 | 60000 | 60000 | 50000 | 40000 | 30000 | 20000 | 10000 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
LCWSP | 8370 | 8311 | 8252 | 8193 | 8134 | 7945 | 7757 | 7568 | 7380 | 7191 | 7002 | 6814 | 6625 | 6437 | 6248 | 6059 | 5871 | 5682 | 5494 | 5305 | 5091 | 4878 | 4664 | 4451 | 4237
Basic Apportionment with Adjustments
IID-SDCWA
IID-MWD
Canal Lining SDCWA
Canal Lining MWD
Southern Nevada
Lower Colorado WSP
PVID Minimum
Total CRA Base Supplies (Million Acre-Feet) |  |  |  | 
2020 | 2025 | 2030 | 2035 | 2040
0.92 | 0.88 | 0.88 | 0.85 | 0.84

## Slide 19: SWP Existing Conveyance Scenario Draft Forecast Table A + Article 21
Chart: Calendar Year
| 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040
Blank Area | 209973.6269 | 209973.6269 | 209973.6269 | 209973.6269 | 154473.9898 | 154473.9898 | 154473.9898 | 154473.9898 | 154473.9898 | 154473.9898 | 154473.9898 | 154473.9898 | 154473.9898 | 154473.9898 | 154473.9898 | 154473.9898 | 154473.9898 | 154473.9898 | 154473.9898 | 154473.9898 | 154473.9898 | 154473.9898 | 154473.9898 | 154473.9898 | 154473.9898
Range | 1811600.6533 | 1811600.6533 | 1811600.6533 | 1811600.6533 | 1400440.842 | 1400440.842 | 1400440.842 | 1400440.842 | 1400440.842 | 1400440.842 | 1400440.842 | 1400440.842 | 1400440.842 | 1400440.842 | 1400440.842 | 1400440.842 | 1400440.842 | 1400440.842 | 1400440.842 | 1400440.842 | 1400440.842 | 1400440.842 | 1400440.842 | 1400440.842 | 1400440.842
Average | 1201749.2418 | 1199919.0879 | 1198088.967 | 1196258.8901 | 837058.1978 | 837058.1978 | 837058.1978 | 837058.1978 | 837058.1978 | 837058.1978 | 837058.1978 | 837058.1978 | 837058.1978 | 837058.1978 | 837058.1978 | 837058.1978 | 837058.1978 | 837058.1978 | 837058.1978 | 837058.1978 | 837058.1978 | 837058.1978 | 837058.1978 | 837058.1978 | 837058.1978
Total Range of SWP Supplies (Million Acre-Feet) |  |  |  |  | 
 | 2020 | 2025 | 2030 | 2035 | 2040
Min | 0.15 | 0.15 | 0.15 | 0.15 | 0.15
Avg | 0.84 | 0.84 | 0.84 | 0.84 | 0.84
Max | 1.55 | 1.55 | 1.55 | 1.55 | 1.55

## Slide 20: Storage Portfolio

## Slide 21
Local Storage Diamond Valley Lake Mathews Lake Skinner Conjunctive Use Programs DWR State Project Reservoirs
Central Valley/SWP Storage
San Luis Carryover
Semitropic Arvin-Edison
Kern Delta
Mojave
CRA Storage DWCV Advance Delivery Lake Mead ICS
Metropolitan’s Storage Programs

## Slide 22: MWD Storage Programs Summary Million Acre-Feet
 | Storage Capacity | Put Capacity* | Take Capacity* | 2016 Est. Starting
Central Valley & SWP | 1.63 | 0.54 | 0.56 | 0.42
Colorado River | 2.39 | 0.65 | 0.60 | 0.22
In-Region | 1.30 | 0.90 | 0.94 | 0.14
Total Dry-Year | 5.32 | 2.09 | 2.10 | 0.77
Emergency | 0.63 | 0.63 | 0 | 0.63
Total | 5.95 | 2.72 | 2.10 | 1.40
*Shows maximum capacities, actual capacity varies based on contract terms

## Slide 23: What Happens if We do Nothing? “Do Nothing” Case Draft Water Balance

## Slide 24: Reliability Measures

## Slide 25: Potential Measures of Reliability
Supply shortages
  Frequency of shortage (a.k.a. probability)
  Size of shortage
  IRP reliability goal: “100% reliability under foreseeable hydrologic conditions”
Storage thresholds
  Minimum storage level
  Average storage level

## Slide 26: Summary of Shortage Probability “Do Nothing” Case Draft Water Balance
Chart: 
| 2040 | 2035 | 2030 | 2025 | 2020
Shortage | 0.59341 | 0.36264 | 0.20879 | 0.065934 | 0.076923
No Shortage | 0.40659 | 0.63736 | 0.79121 | 0.93407 | 0.92308

## Slide 27: Summary of Ending Dry-Year Storage “Do Nothing” Case Draft Water Balance
Chart: 
| 2040 | 2035 | 2030 | 2025 | 2020
Less Than 1 MAF | 0.84615 | 0.6044 | 0.31868 | 0.16484 | 0.10989
Greater Than 1 MAF | 0.15385 | 0.3956 | 0.68132 | 0.83516 | 0.89011

## Slide 28: Observations “Do Nothing” Case Draft Water Balance
The “do nothing” approach is not sustainable
Shortage probability and size both increase over time
  Total retail demands increase over time
  Constant or decreasing local and imported supplies
Storage quantity decreases over time
  Less water to store
  Higher needs for storage to balance supplies and demands
Significant resource investments are needed

## Slide 29: What Happens if We Develop the 2010 IRP Update Targets? Current IRP Approach Draft Water Balance

## Slide 30: Current IRP Development Targets
Water Use Efficiency
Achieve a 20% reduction in GPCD as a region by 2020
Local Resources
Develop ~100 TAF through incentives and partnerships
SWP
Seek short, mid, and long-term Delta improvements
CRA
Develop Dry-Year supply programs to fill the aqueduct when needed

## Slide 31: Targeted IRP Development Current IRP Approach
Chart: Calendar Year
| 2020 | 2025 | 2030 | 2035 | 2040
20x2020 | 130000 | 130000 | 130000 | 130000 | 130000
Local Augmentation | 15000 | 40000 | 40000 | 40000 | 40000
Delta Improvements | 350000 | 350000 | 375000 | 375000 | 375000
Targeted Development (Thousand Acre-Feet) |  |  |  | 
2020 | 2025 | 2030 | 2035 | 2040
495 | 520 | 545 | 545 | 545
Delta Improvements
Local Augmentation
Water Use Efficiency

## Slide 32: Summary of Shortage Probability “Do Nothing” Case Draft Water Balance
Chart: 
| 2040 | 2035 | 2030 | 2025 | 2020
Shortage | 0.59341 | 0.36264 | 0.20879 | 0.065934 | 0.076923
No Shortage | 0.40659 | 0.63736 | 0.79121 | 0.93407 | 0.92308

## Slide 33: Summary of Shortage Probability Current IRP Approach Draft Water Balance
Chart: 
| 2040 | 2035 | 2030 | 2025 | 2020
Shortage | 0.021978 | 0.010989 | 0 | 0 | 0.021978
No Shortage | 0.97802 | 0.98901 | 1 | 1 | 0.97802

## Slide 34: Summary of Ending Dry-Year Storage “Do Nothing” Case Draft Water Balance
Chart: 
| 2040 | 2035 | 2030 | 2025 | 2020
Less Than 1 MAF | 0.84615 | 0.6044 | 0.31868 | 0.16484 | 0.10989
Greater Than 1 MAF | 0.15385 | 0.3956 | 0.68132 | 0.83516 | 0.89011

## Slide 35: Summary of Ending Dry-Year Storage Current IRP Approach Draft Water Balance
Chart: 
| 2040 | 2035 | 2030 | 2025 | 2020
Less Than 1 MAF | 0 | 0 | 0 | 0 | 0.032967
Greater Than 1 MAF | 1 | 1 | 1 | 1 | 0.96703

## Slide 36: Observations Current IRP Approach Draft Water Balance
Significant resource investments are needed to achieve the current IRP Targets
Existing supplies need to maintained
  Colorado River Aqueduct
  Local supply production
Compared to the “Do Nothing” Case
  Reliability measures improve
  Storage measures improve
  Challenges still exist in the shorter term

## Slide 37: What Potential Changes to the Current IRP Targets are Needed?
Adjust targets to address shorter term imbalances
Adjust targets to ensure sufficient storage levels
Ensure an adequate supply buffer
Refine and improve implementation approaches and policy to ensure development

## Slide 38: Next Steps

## Slide 39: Next Steps – Water Tomorrow
Phase 1: IRP Technical Update
  Finalize Results: October 2015
  Public Outreach Workshop: October 22nd
  IRP Committee considers Technical Update adoption: December 2015
  IRP Technical Update Final Report: Early 2016
Phase 2: Investigate Policy Implications
  Kick-off: Early 2016